| FURFUR ALDEHYDE |
| --- |
| 20. FURFURALDEHYDE |
| Production capacity | Quantity:, 450 MT pa Value: Rs. 202 Lakhs |
| Quality standards | IS 13322 |
| User profile | Manufacture of furan derivatives, extractive distillation of hydrocarbons, decolorizing agent for wood resin, reactive solvent, mfr of varnishes, insecticide, reagent in analytical chemistry, refining of animal and vegetable oils etc |
| Land & building | 5 acres land, 730 sq mts covered area – Rs 10 lakhs |
| Machinery & Equipment: | Digesters, stripping column, dehydrating colum, dehydrating column heat exchanger, decanter, distillation still, storage tanks, conveyors, water softener plant, cooling water tower, heat exchanger, boiler, ETP, motors, pumps, diesel genset, fittings and accessories, testing equipment, installation, MS platform etc – Rs 71 lakhs |
| Raw materials per month, for 3000 pairs | Corn cobs, bagasse, peanut hulls, rice husk, corn stalks, cotton seed hulls etc. Sulphuric acid, misc chemicals, MS drums – Rs 9.07 lakhs |
| Utilities per month | Power-1.92 lakhs Water- Rs. 4000 pm |
| Other contingent expenditure per month | Rs. 23,500 |
| Staff / labour : | Manager, 3 supervisors, boiler operator, chemist, accountant, office assistant, 9 skilled workers , 24 unskilled workers – total pm 1.23 lakhs. |
| Working capital required( for 3 month) | Rs. 37.42 lakhs |
| Total capital investment | Rs 122.42 lakhs |
| Cost of production per year | Rs. 175.75 lakhs |
| Turnover per year | Rs. 202.5 lakhs |
| Net profit | Rs. 27.75 lakhs |
| Rate of return | 22% |
| Break even | 50% |